## Slide 2: Windows 7 : Mobile Broadband
Hongming (Harry) Song
Program Manager
Hardware Innovation Center
Microsoft Corporation

## Slide 3: Agenda
Windows 7: Mobile Broadband Overview
Mobile Broadband Driver Model
Mobile Broadband Service API
Logo Requirements
Demo
Call To Action

## Slide 4: Terminologies
Mobile Broadband (MB) is also referred as
  Wireless WAN
  WWAN
  MB
Mobile Broadband Driver is also referred as
  IHV Miniport Driver
  MB Driver
  Miniport Driver

## Slide 5: What Is New?
Simple out-of-box connection experience for Mobile Broadband
  Similar to WLAN, VPN and Dial-up
Driver Model for Mobile Broadband Devices
Mobile Broadband APIs
Logo Program for MB Devices

## Slide 6: Architecture
WWAN Miniport Driver
NDISUIO
3rd Party
Connection Manager
WWAN Service
Profiles
WWAN Miniport Driver
MB Miniport Driver
User Mode
Kernel Mode
Mobile Broadband Driver Model
Command
Line Interface
Mobile Broadband API
View Available
Network UI
Properties UI
Connection Flow
Experience UI
Session 0
Provided by:
Microsoft
ISV
OEM
IHV
Notes: This architecture diagram illustrates the control path of the Mobile Broadband stack. The data path is through the NDIS send/receive and is not captured in this block diagram.
Mobile Broadband Driver Model is newly introduced in Windows 7 for Mobile Broadband devices.
Mobile Broadband Driver Model defines the kernel mode interfaces that the IHV drivers need to implement and behavior that the drivers need to comply with. We will discuss in detail about the MB driver model specification in this session.
NDISUIO is a kernel mode component that is responsible for User mode IO for the WiFi. In Win7, this is extended to handle Mobile Broadband devices OID and event notification queuing between user mode and kernel mode. As the primary objective of NDISUIO is to provide a reliable control transport channel between user mode service and kernel mode drivers, in the upcoming slides, for simplicity sake this component will not be explicitly shown.
As all other Windows Services, WWANService is in Session 0. WWANService manages the device, network and connectivity functionalities of Mobile Broadband devices in the User Mode. In addition, WWAN Service, using state machine implementation takes care of PIN, SMS as well as profile related functionalities in addition.
The upper edge of WWAN Service provides Mobile Broadband API to the Windows 7 user mode applications. 3rd Party Connection Managers and applications will be using the Mobile Broadband API for managing and using the Mobile Broadband devices.

## Slide 7: Mobile Broadband Driver Model

## Slide 8: Driver Model
Supports packet-switched data connectivity over the Wireless WAN (3GPP/3GPP2) devices
Interconnect agnostic – Works on USB, PCMCIA/PC Card and any other interconnect technology
Introduces new NDIS Medium – NdisMediumWirelessWAN
Framework designed for slow response AT command based devices
Based on NDIS6.20 miniport driver model
Notes: Old mode was ethernet emmulation, now new WWAN model

## Slide 9: NDIS6.20 – Data Path
IHV Miniport Driver
NDIS 6.0
TCP/IP Stack
Send / Receive
802.3 Frames
NDIS 6.20
TCP/IP Stack
IHV Miniport Driver
Send / Receive
IP Frames
DHCP Emulation
ARP Emulation
Windows Vista
Windows 7
Windows 7 IHV Miniport Drivers for Mobile Broadband can
Take advantage of raw IP support in send/receive path
Eliminate DHCP and ARP spoofing in miniport drivers
Write less code and focus more on Quality

## Slide 10: Control Path Functionalities
MB Driver Model defines the following control path functionalities
  Device State Management
  Connectivity Management
  Radio Control
  SMS (Short Message Services)
  PIN
  Provisioned Contexts
  Vendor Specific, e.g. Service Activation
Notes: Device state management == profiles,
Connectivity management ==
Radio Control == driver can physically turn on/off devices
Provisioned Contexts = username/password & APN

## Slide 11: Control Path DDIs
WWAN Service uses NDIS OIDs for control requests (SET or QUERY) to miniport drivers
Asynchronous semantics for slow control devices
  Designed for AT command-response based modems

## Slide 12: Design For Deployment
Consider the following deployment scenarios while developing Win7 Drivers
  Upgrade of Windows Vista to Windows 7
    Ensure Windows 7 drivers can handle the Vista based Connection Managers
  Devices can be used in Windows 7 as well as down-level Windows
    Develop single firmware supporting all Windows
Notes: Vista CM using OID calls to legacy NDIS drivers.
Single firmware package.

## Slide 13: Design For Deployment
Driver distribution through Windows Update
  Must be INF based installation
  Firmware upgrades must be handled through Device Co-Installers
Notes: Plug in device -? PNP Event -> search driver store, WU, and media. (copies into windows.inf) -> reads INF
Copies files to appropriate location copies .sys files to sys32.drivers; co-installer specifies new reg values & INF.

## Slide 14: Mobile Broadband API

## Slide 15: Supported Functionality
Device management
Radio state management
Connectivity management
Profile management
SMS
PIN
Custom Activation
Vendor specific operation
Profile API provides branding opportunity for operators
Custom service activation
  Pass-through API for vendor specific service activation
  Payload data is passed through to Mobile Broadband Driver
  Needs support from MB driver

## Slide 16: Custom Features
Framework provides vendor-specific API to implement custom features
WWAN Service provides a pass-through control path for Windows 7 applications to communicate with IHV drivers
Usage Example
  SIM Tool Kit Commands
  USSD Commands
  Phone Book Commands
  Voice Commands
  And more…
MB Miniport Driver
WWAN Service
3rd Party Apps/Connection Managers
OID_WWAN_VENDOR_SPECIFIC
NDIS_STATUS_WWAN_
VENDOR_SPECIFIC
Set VendorSpecific
OnEventNotification

## Slide 17: Mobile Broadband (MB) Logo
Mobile Broadband Logo Program is created with end-user experience in mind - several new approach of testing to ensure the user experience is good and consistent
New testing approach are:
  End-to-End scenario testing
  Live network testing
The logo requirements are also structured to support the new approach
  There are 12 logo requirements that are classified into 4 categories
Functionality
Conformance
Serviceability
Performance
Notes: Mobile Broadband Logo Program is introduced with the introduction of native support for Mobile Broadband Networking Technology (a.k.a, WWAN or 3G Networking) in Windows 7.
In the past, different vendors implement Mobile Broadband differently: either emulating Ethernet or Modem.
  This is a non-ideal solution as the provide different type of user-experience to the end-users depending on the device they use.
In Windows 7, the driver model for Mobile Broadband devices is standardized with the introduction of the new Mobile Broadband Driver Model Specifications.
The Mobile Broadband Logo Program is created specifically to validate driver implementation against the Mobile Broadband Driver Model Specifications to ensure the stability and reliability of the drivers.
  Once the driver is certified through this program (WHQL), it can be easily distributed to the end users via the Windows Update mechanism build into every Windows client.

## Slide 18: Demo

## Slide 19: Call To Action
Develop NDIS6.20 drivers compliant with Mobile Broadband Driver Model
  MB devices must be NDIS6.20-based to get logo.
  Refer to Mobile Broadband Whitepaper for multi-stage development model
  Design drivers taking deployment scenarios into consideration
Test commercially deployed Mobile Broadband device solutions in Windows 7
Review Mobile Broadband device logo requirements and send us feedback
Contact us at win7mb@microsoft.com

## Slide 20: Resources
Mobile Broadband Logo Requirements on https://winqual.microsoft.com/
  Log in, click on the Logopoint link on the left side menu, and search for “MBN” requirements
WDK Documentation on MSDN
  Porting NDIS 5.x Drivers to NDIS 6.0 - http://msdn.microsoft.com/hi-in/library/ms795567(en-us).aspx
  IP Helper - http://msdn.microsoft.com/hi-in/library/bb742902(en-us).aspx
WDK documentation
  Mobile Broadband Driver Model Specification
  Mobile Broadband Driver Test App (WwanDriverTestApp)
  NDIS 6.20
Windows Logo Kit (WLK)
  Mobile Broadband Logo Tests
WHDC Web site at http://www.microsoft.com/whdc/default.mspx
  Mobile Broadband Driver Development White Paper

## Slide 21
© 2008 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.