## Slide 1: Connection Manager Integration with Mobile Broadband

## Slide 2: Contents
Introduction
Service Activation
  Device-Based Integration
  Portal-Based Integration
  Manual Service Activation
Access Point Name (APN) Database (DB) Integration
  APN DB from IHV
  APN DB from OEM
  Manual Entry
Call to Action
Resources

## Slide 3: Introduction
This presentation shows how to use the mobile broadband API to develop lightweight utilities and custom connection managers for service activation and APN-DB integration.
These lightweight utilities and custom mobile broadband connection managers are provided by:
  Independent software vendors (ISV).
  Original equipment manufacturers (OEMs), such as PC manufacturers.
  Mobile network operators (MNOs).
  Independent hardware vendors (IHVs), such as mobile broadband device manufacturers.
More information about developing connection managers and similar utilities by using the mobile broadband API is available on the “Resources” slide.

## Slide 4: Service Activation
Three solutions for service activation:
  Device-based integration
  Portal-based integration
  Manual service activation

## Slide 5: Device-Based Integration
Activation logic is implemented by IHV device firmware or driver.
Mobile broadband stack provides framework to activate service.
Activation module calls mobile broadband API to activate service.
Data structure passed down to driver in the API are defined between MNOs and IHV.
Mobile Broadband Device
WWAN Service
Activation Module
Activate()
    OID_WWAN_SERVICE
    _ACTIVATION
    NDIS_STATUS_WWAN_
    SERVICE_ACTIVATION
OnActivation
Complete()
Activation
Logic
Provided by:
Microsoft
ISV
MNO
IHV

## Slide 6: Portal-Based Integration
MNO implements activation logic.
Activation module communicates with MNO portal for service activation.
Activation module uses IMbnVendorSpecificxxx mobile broadband API to pass data directly to driver to activate service.
Data structure passed down to driver in the API are defined between MNO and IHV.
Mobile Broadband Device
WWAN Service
Activation Module
SetVendor
Specific()
    OID_WWAN_
    VENDOR_SPECIFIC
    NDIS_STATUS_WWAN_
    VENDOR_SPECIFIC
OnSetVendor
SpecificComplete()
MNO
Portal
Activation request
Activation status
Activation
Logic
Provided by:
Microsoft
ISV
MNO
IHV

## Slide 7: Manual Service Activation
Activation Module
Mobile Broadband Device
WWAN
Service
Launch connection manager for subscription information.
Get all subscription information in a single user interface.
Talk to MNO to activate service.

## Slide 8: APN Database (DB) Integration
Three possible integration solutions:
  APN DB from IHV (device provisioning)
  APN DB from OEM
  Manual

## Slide 9: APN DB from IHV
IHV provisions APN on the device.
Mobile broadband stack communicates with the device to get APN.
No additional third-party software is required.
Mobile Broad-
band Device
WWAN
Service
Create profile
DB
Clicks connect
VAN UI
Request for APN information
Response : APN
Connect

## Slide 10: APN DB from OEM
WWAN
Service
GetSubscriberInformation()
CreateConnectionProfile()
Lookup APN DB
[Key : Home Provider ID]
APN Module
APN
DB
APN module uses mobile broadband API to create the profile.

## Slide 11: Manual Entry
WWAN
Service
Connect
Clicks on connect
VAN UI
UI to get APN,
User name, Password
This fallback option is used only if APN is not available from either device or activation module.
APN, User name, Password

## Slide 12: Call to Action
Use mobile broadband API to develop lightweight utilities for activation and APN DB integration.
Migrate your existing connection manager to use the mobile broadband API.
Partner with the IHV and MNO to define custom data to be sent to the device by using the vendor-specific mobile broadband API.

## Slide 13: Resources
Mobile Broadband Portal
  http://www.microsoft.com/mobilebroadband
Questions?
  win7mb@microsoft.com

## Slide 14
© 2009 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista, and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries. The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.