## Slide 2: Wireless LAN Enhancements In Windows 7
Hong Liu
Senior Program Manager
Microsoft Corporation
Billy Anders
Group Program Manager
Microsoft Corporation

## Slide 3: Agenda
Introduction
Program overview
Architecture
Coding sample
Demos
Q&A

## Slide 4: Market Drivers
Pervasiveness of WiFi networks
High penetration of laptops with WiFi
Proliferation of WiFi capable devices
Ever increasing growth in mobile workers
Emergence of innovative scenarios based on IP endpoints
Wireless ubiquity + mobile computing = Mobile Wireless PAN

## Slide 5: Win7 Enhancements
Foundational improvements to WiFi
  Significant reduction in resume time
New support for wake-on-wireless LAN
New WiFi-PAN platform
  Software Access Point (SoftAP)
  Virtual WiFi (VWiFi)
New logo requirements for Windows 7

## Slide 6: SoftAP/VWiFi Functionality
Enables dual STA-AP modes on the same WiFi NIC
  Primary NIC in STA mode; secondary NIC in AP mode
  Allow exactly one SoftAP per Windows 7 laptop
  Both operate on the same radio frequency channel
Provides enhanced security via WPA2-PSK-AES
  Support for machine generated or user-provided key
Managed via group policy and Netsh for IT administrators
APIs provide developers full control to create new applications
Required for Win7 logo

## Slide 7: Enabling Scenarios
Inbox scenario
  SoftAP used for provisioning WPS capable devices onto non-WPS networks
3rd party applications using hosted network APIs
  Device connectivity to Windows 7 laptop
  PC connectivity to Windows 7 laptop
  Internet sharing for device and PC through Windows 7 laptop
  Direct high-definition streaming

## Slide 8: SoftAP/VWiFi Architecture
WiFi Hardware
IHV Miniport Driver
(ExtSTA, NetMon, ExtAP)
NDIS Port 1
VWiFi Filter Driver
VWiFi Bus Driver
VWiFi Miniport Driver
NDIS Port 0
NWiFi Filter Driver
VWiFi Filter Driver
Networking Stack
Primary Adapter
Secondary Adapter
Networking Stack
WLAN Service
Private
Interface
Legend:
Control
Data
Control
& Data
Netsh
Provided by:
Microsoft
ISV
IHV
OEM
WCN
ISV App
IHV App
OEM App
Hosted Network APIs
User Mode
Kernel Mode

## Slide 9: Code Sample How to start and stop SoftAP
// open handle
dwError = WlanOpenHandle( WLAN_API_VERSION_2_0 , NULL, &dwNegotiatedVersion, &hClientHandle);
// check return value
// configure softap
dwError = WlanHostedNetworkInitSettings( hClientHandle, &FailReason, NULL );
// check return value
// start softap
dwError = WlanHostedNetworkStartUsing( hClientHandle, &FailReason, NULL ) ;
// check return value
// use softap
// stop softap
dwError = WlanHostedNetworkStopUsing( hClientHandle, &FailReason, NULL ) ;
// check return value
// close handle
dwError = WlanCloseHandle(hClientHandle, NULL);

## Slide 10: SoftAP/Virtual WiFi
Billy Anders
Group Program Manager
Windows Networking
demo

## Slide 11: Demo Applications
Simple SoftAP management prototype
Wireless Connection Sharing prototype
Zune desktop application prototype
End-to-end wireless photo experience

## Slide 12: Call To Action
Develop SoftAP enabled applications using Windows 7 hosted network APIs
Add WiFi and WPS capabilities to devices
Test your WiFi devices with Windows 7 for great interoperability
Contact Microsoft for specification
  Hosted network API specification
  Driver model specification
Provide feedback to improve the product!

## Slide 13: Additional Resources
Documentation with Windows 7 Beta release
  SDK with sample code and documentation
  WDK with sample driver and documentation
Related sessions
  CON-C653: Wireless Connect Now for Wireless Devices
E-mail us: 80211_fb@microsoft.com

## Slide 14: Q&A
Thank you!

## Slide 15: Please Complete A Session Evaluation Form Your input is important!
Visit the WinHEC CommNet and complete a Session Evaluation for this session and be entered to win one of 150 Maxtor® BlackArmor™ 160GB External Hard Drives 50 drives will be given away daily!
http://www.winhec2008.com
BlackArmor Hard Drives provided by:

## Slide 16
© 2008 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.