## Slide 1: Home Media Transports
Dr. Anton Monk
CTO
Multimedia over Coax Alliance

## Slide 2: Agenda
Introduction to Multi-room DVR
Home Networking Requirements
MoCA as Industry Standard
MoCA Field Trial Data
MoCA Features

## Slide 3: Multi-Room DVR – The “Killer App”
Kitchen
Family Room
Master Bedroom
Kids Bedroom
Office/Den
Media Center PC
WebPad
Client STB
802.11 Wireless AP
Broadband Multimedia
Coax
Coax
Client STB
802.11 Bridge
Home Server - DVR
Cable, Telco
DBS

## Slide 4: Home Networking Requirements (1 Of 3)
Reliable and ubiquitous
  Works where your TV and STB works
  Clean, dedicated, shielded medium with open frequency band
Simple to install
  No new wires (or splitters)
  Retail or non-truck roll solution
High performance: >95% solution
  With reasonable remediation for remaining <5%
  Net Throughput > 100 Mbps
  Packet Error Rate < 1e – 5
    Delay < 10 msec; Jitter < 1 msec

## Slide 5: Home Networking Requirements (2 Of 3)
Delivers “no excuses” HDTV and DVD quality
  Supports and coexists with:
    Cable, DBS, Terrestrial
    Telco, CE, PC
  Supports content protection, key protocols, high data rates
  Consistent with DLNA, DTCP-IP, CableHome, UPnP

## Slide 6: Home Networking Requirements (3 Of 3)
Meets all key market requirements
  Enables cost-effective multi-room DVR
    Including HDTV
  Satisfies any-room access to all home media:
    Video, audio, voice
    Data, gaming, control
  Saves installation and deployment costs
  Future-proof support of >1 Gbps home network

## Slide 7: Industry Standard (1 Of 3)
Open, industry-driven alliance, promoting:
  Networking of digital video and entertainment
  Through existing coaxial cable in the home
Only alliance with board-of-directors representation from:
  Telco, Cable, DBS, and Retail
Field tested and deployed…
43 members and counting…

## Slide 8: Industry Standard (2 Of 3)
Field tests of 250 homes
  >110 Mbps net throughput
  …in 97 percent of all outlets
Completed 4 certification waves with 17 certified products
MoCA MAC/PHY 1.0 approved
  Distributed to members in January 2006
Deployed in well over 200,000 homes
  In U.S., to date

## Slide 9: Industry Standard (3 Of 3)
Promoter Members Associate and Affiliate Members

## Slide 10: MoCA Field Trial Data Rate Results (1 Of 2)
250 homes, 15 cities, 120 zip codes, 5K+ person-hours
>110Mbps net/usable > 97% of outlets without remediation
0
10
20
30
40
50
60
70
80
90
100
0
50
100
150
200
250
% Paths
Mbps
PHY Rate
Throughtput (MAC) Rate
Performance: Percent of Paths versus Bit Rate
100 Mbps

## Slide 11: MoCA Field Trial Data Rate Results (2 Of 2)
Packet Error Rate less than 10-6
Latency less than 5ms
Net usable (MAC) data rates:
  With no changes to home coax system:
    97% of all paths in all homes achieved ≥ 110 Mbps
  With simple remediation to installed coax cable system:
    100% of homes achieved ≥ 95 Mbps on every path in the home
Validated in mass deployment by Verizon FiOS service

## Slide 12: MoCA Features (1 Of 2)
Physical Layer
  Automatically pre-equalizes modulation to path frequency response
  Each path independently and continuously optimized
  Up to 270 Mbps PHY
  PER < 10-6 (no retransmissions, low latency)

## Slide 13: MoCA Features (2 Of 2)
MAC Layer
  Fully scheduled protocol (no collisions)
  Automatically selected and mobile network coordinator
  Support for admission control and parameterized QoS
  Privacy
  >100Mbps net (UDP) throughput

## Slide 14: MoCA Frequency Coexistence (1 Of 2)
Coax and splitters support reliable communications above 860 MHz
Coexistence with existing services (next slide)
MoCA is the only solution which…
  …meets the strict requirements of a multimedia home network
  …including coexistence with all service providers’ frequency plans

## Slide 15: MoCA Frequency Coexistence (2 Of 2)
1
54-806/860
Off-Air/CATV
5-42
Upstream
CM
MoCA
MoCA
MoCA
…
MoCA
950-2150
Satellite L-Band
2
54-806/860
Off-Air/CATV
5-42
Upstream
CM
Coexistence with existing services
  CATV Cable Modem upstream (5 to 42 MHz)
  UHV/VHF video and Cable Modem downstream to 806/860 MHz
  DBS services from 950 to 2150 MHz

## Slide 16: Summary (1 Of 2)
Home usage model
  Room-to-room, peer-to-peer, full mesh connectivity
  >100 Mbps net throughput
  No-excuses, glitch-free video
  Consumer- or Service-provider enabled
Medium for whole home reliable, maintainable coverage
  Connections collocated with TVs and other video devices
  Coexists with existing services and devices
  Medium used “as is” – no new cables, splitter replacements

## Slide 17: Summary (2 Of 2)
Real world validation
  >110Mbps in 97% of all connections
    Reasonable remediation for other connections
  Mass deployment by Verizon FiOS service
  Deployment expected by other operators 2H07
MoCA meets all requirements for home networking digital entertainment without compromise

## Slide 18: Additional Resources
Web Resources
  MoCA Alliance: http://mocalliance.org
  Whitepapers: http://www.mocalliance.org/en/industry/ whitepapers.asp
Contact
anton.monk@mocalliance.org